## Slide 1
Giải pháp HW xử lý cho AI-Vision
1. Hardware overview
2. Deployment solution
3. Complexcity and Optimization
4. Benchmark result
5. Conlcusion

## Slide 2
1. Hardware overview
Architecture
  INTEL: SKYPE-COFFE-ICE... LAKE
  SHAVE: Hybrid RISC-DSP-GPU VLIW architecture
  TPU
  GPU
  FPGA
Parameter of performance
  OPS: Operation persion second
  TOPS – (INT8, INT4): Tera (10^12) operation (INT8, INT4) per second
  TFLOPS – (FP32, FP16, Mix): Tera operation (FP32, FP16, Mix) per second
  FLOPS(FP32) = ~ 2 x FLOPS(FP16) = ~ 23 x FLOPS(Mix) = ~ 24 TOPS(int8) = ~ 25 TOPS (int4)

## Slide 3
Hardware overview
No | Board | Vendor | OPS |  | GOP/W | Frameworks | Prices (eval..)
 |  |  | FLOPS | TOPS |  |  | 
1 | RTX 2080 Ti | NVIDIA | 13.45 TFLOPS (FP32) | N/A | N/A | TensorFlow, PyTorch, Caffe,MXNet, Theano | 2000$
2 | Tesla T4 | NVIDIA | 8.1 TFLOPS (FP32) 65 TFLOPS (Mix) | 130 TOPS (int8) | 1850 | TensorFlow, PyTorch, Caffe,MXNet, Theano | 3200$
3 | Tesla V100 PCIe | NVIDIA | 14 TFLOPS (FP32) 112 TFLOPS (Mix) | N/A | N/A |  | 13000$
4 | U250 | Xiliinx | N/A | 33.3 TOPS (int8) | 151 | Caffe, tensorflow | 6995$
5 | Jetson Nano | NVIDIA | 472 GFLOPS | N/A | 94.4 | TensorFlow, PyTorch, Caffe,MXNet, Theano | 99$
6 | Coral Edge TPU | Google | N/A | 4 TOPS (int8) | 2000 | TensorFlow Lite | 115$
7 | AI Core X, Movidius | AAEON (ASUS) | N/A | 1 TOPS (int8) | 400 | Caffe, tensorflow | 79$
8 | ZCU104 | Xiliinx | N/A | 2.4 TOPS (int8) | N/A | Caffe, tensorflow | 895$
9 | Sipeed MAIX | Seeed Studio (China) | N/A | 250 -500 GOPS (int8) | 833.3 | N/A | 5$ (chip)
10 | Hailo | HAILO | N/A | 26 TOPS (int8) | 15500 | N/A | N/A
FLOPS(FP32) ~ 2 x FLOPS(FP16) ~ 23 x FLOPS(Mix) ~ 24 TOPS(int8) ~ 25 TOPS (int4)

## Slide 4
Hardware overview
Desktop History: Increase TFLOPS ~30% each year
Prices 2018 (Full GPU+CPU…): ~200$/TFLOPS; N/A$/TOPS
GTX TITAN, 999$
4.5 TFLOPS
GTX TITAN X, $ 999
6.1 TFLOPS
Titan Xp $1200
10.8 TFLOPS
RTX 2080 Ti, $ 1199
13.4 TFLOPS
2/2013
3/2015
4/2017
9/2018
Ref: https://en.wikipedia.org/wiki/List_of_Nvidia_graphics_processing_units
???? $1200
~22.5 TFLOPS
2020

## Slide 5
Hardware overview
Workstation History: Increase ~50% each year
Prices 2017 (Full DGX): ~1000$/TFLOPS; N/A$/TOPS
Prices 2018 (T4 support INT4, Dell R740+4Cards = 13200$): ~400$/TFLOPS; ~12$/TOPS
Tesla
2.5 TFLOPS
Femi
4.1 TFLOPS
Kepler
5.5 TFLOPS
Maxwell
7.3 TFLOPS
6/2008
7/2011
11/2014
8/2015
Ref: https://en.wikipedia.org/wiki/List_of_Nvidia_graphics_processing_units
DGX-1: 8 cards => 129k$;
Only T4 supporting with INT4
Volta
14.9 TFLOPS
6/2017

## Slide 6
Hardware overview
Processing with type precision depend on DEVICE:
  V100 and other Nvidia not support for INT8/INT4

## Slide 7
2. Deployment solution (1)

## Slide 8
Deployment solution (2)
FOG/EDGE solving: Delay/Bandwidth/Responding

## Slide 9
Hardware & SDKs

## Slide 10
Deploy Algorithm with Any Devices?
Problem in Cloud/Fog:
  Framework: Tensorflow, Keras, Pytorch, Mxnet, Caffe ....
Problem in Edge:
  SDK in edge: JetsonSDK, DNNDK, OpenVINO, SNPE....
  Not support User-defined Neural Network layers

## Slide 11
3. Complexcity of Application AI
Computing in AI: CNN, RNN...
=> 90% time-processing of Application involve NN

## Slide 12
Complexcity of Algorithm AI
OPS/Layer = 2 * MAC = 2 x DimFM[i]2 x NumFM[i] x NumFM[i-1] x DimSten[i]2

## Slide 13
Complexcity of Algorithm
Layer 0:
Layer 1:
Layer 105:

## Slide 14
How to reduce cost
1. Market reduce prices of TOPS
2. Optimize Algorithm

## Slide 15
Optimize Algorithm
Challenges: MAC depend on Size-NN, so
1. FP Precision to ultilize HW new architecture
  Framework support change precision:
    Support to change to FP16, INT8, INT4?
  If not:
    Build from zero, not using pretrain: Data?
2. Algorithm to reduce MAC
  Reduce size filter, reduce layer => Has DONE, but always Accuracy DOWN
  KEY: Innovation about Architect NN&DATA to get SOTA in optimizing

## Slide 16
4. Benchmark result
STT | Algorithm | Complexity | Layers | Performance (FPS) |  |  |  |  |  |  |  | Note
 |  |  |  | 2080 Ti | V100 | U250 | ZCU 104 | Jetson Nano | Coral Edge TPU | Pi 4 | Hailo | 
Detection | Yolov3 416x416 | 140.69 GFLOPS | 106 | 60 | 80 | N/A | 29 | 2 | - | - | - | Darknet-53
 | Yolov3-tiny | 5.56 GFLOPS | 24 | 240 | 320 | N/A | N/A | 25 | - | - | - | x4 times more with yolov3
 | Yolov2-voc 608x608 | 62.94 GFLOPS | 30 | 120 | 160 | 125 | 58 | 4 | - | - | - | Darknet-19 https://arxiv.org/pdf/1811.05588.pdf
 | SSD Mobilenet v2 | 13.2 GFLOPS |  |  |  |  | 116 | 39 | N/A | 10 | - | 
Classification | VGG16 – FP32 | N/A | 16 | 169 | 233 | 476 | 73 | N/A | - | - | - | 
 | VGG19 - 224x224 | N/A | 19 | N/A |  | N/A | N/A | 10 | 3.2 | - | - | 
 | ResNet-50 – FP32 | 15.5 GFLOPS | 50 | 286 | 368 | 1200 | 124 | 36 | - | - | 672 (INT8) | 
 | Arcface | 24G FLOPs | 100 | 50 |  |  |  | N/A | - | - | - | iccv19-challenge: ResNet100FC-IR): 24G FLOPs
Pose Estimation | OpenPose | 100 GFLOPS |  | 22 |  |  | 37.2 | 10 (MobileNet) | - | - | - | 1280x960 MobileNet Thin I7-8700K: 25 ¦ 2080Ti: 52.7 FPS
 | AlphaPose | N/A |  | 23 |  |  |  | N/A | - | - | - | 
Action recognition | I3D-TSN | 16.3 BFLOPS |  | 20 |  |  |  | N/A | - | - | - | Backbone: BN-Inception 11.3M
 | LSTM | 8.42 MFLOPS |  |  |  |  |  | N/A | - | - | - | 0.53M paprams
U250~2080Ti; U250 = 2 x ZCU 104

## Slide 17
CAPEX For Production
 | VHT |  | Parner working with IDC |  | Avnet-Xilinx ZCU | Brodmann17 | Smarty | Note
 | Current | Target 1 year (10x) | Futurix | XRVision |  |  |  | 
vSmartGate | 40.000.000 | 4.000.000 | N/A | N/A | N/A | N/A | 160.000.000 | 2 camera/1 cards
vSmartSafe | 80.000.000 | 8.000.000 | N/A | N/A | N/A | N/A | N/A | 1 camera/1 cards
vSmartAnalytic | 20.000.000 | 2.000.000 | 330$ | 250$ | 450$ | N/A | N/A | 4 camera/1 cards

## Slide 18
5. Conclusion
1. Thử nghiệm deploy hệ thống trên 02 boards Jetson nano (Nvidia) and i.MX8M MINI SOM (Gyrfalcon) để đánh giá hiệu năng và tính khả thi triển khai.
2. Xây dựng thiết kế hệ thống dựa trên 02 loại chip AI là Lightspeeur (Gyrfalcon) và Myriad (Intel) để so sánh hiệu năng và giá.

## Slide 19
Thank you

## Slide 20
Phụ lục: OpenVINO SDK

## Slide 21
Phụ lục: Qualcomm SDK

## Slide 22
Phụ lục: DNNDK

## Slide 23
Phụ lục: Jetson SDK