## Slide 1: HW AI: the first look
Presenter: Cuong Pham (cuongpt12)
Nov-12-2019

## Slide 2: contents
Overview
Compare ASIC & FPGA
  Extensions to model
  Debug Controller
Complexity of CNN
Boards survey
Conclusion

## Slide 3: overview
ASIC stands for Application Specific Integrated Circuit.
It’s built from logic gate (physical layer is transistor).
Basic gates
Logic function
Storage element
processor
Specific datapath
Memories
CPU
GPU
FPGA

## Slide 4: Overview (intel ice lake)
CPU
  On average 18% increase in IPC in comparison to 2015 Skylake running at the same frequency and memory configuration
  L1 instruction/data cache: 32KB/48 KiB; L2 cache: 512 KiB
  Dynamic Tuning 2.0 which allows the CPU to stay at turbo frequencies for longer
  Intel Deep Learning Boost, used for ML/AI inference acceleration Gen 11
GPU
  Gen 11 GPU with up to 64 execution units 4K@120Hz, 5K, 8K display output
  Up to 1.15 TFLOPS of computational performance
  Two HEVC 10-bit encode pipelines, either two 4K60 4:4:4 streams simultaneously or one 8K30 4:2:2
  Integer scaling

## Slide 5: Overview (SHAVE)
Hybrid RISC-DSP-GPU VLIW architecture
128-bit vector arithmetic
20 GFLOPS computational power (v2) (v3 x20-30 times)

## Slide 6: Overview (TF)
TPU is coprocessor. It need other processor as master.
256x256 ALU/MAC (65536 elements)
Can perform matrix multiplication and convolution

## Slide 7: Overview (GPU)
Newest architecture is Maxwell.
It can contain thousands of CUDA cores and offers up to tens TOPS

## Slide 8: Complexity of CNN
NOTE: 1 MAC (multiply-accumulate) = 2 Operations

## Slide 9: Complexity of CNN (yolov3)
Layer 0:
Layer 1:
Layer 105:

## Slide 10: Boards survey
No. | Board | Vendor | feature |  | frameworks | Prices (eval..) | Power (W) | Power efficiently (GOP/W)
 |  |  | Chipset | OPS |  |  |  | 
1 | Jetson Nano | NVIDIA | Quad-core ARM Cortex-A57 128-core NVIDIA Maxwell™ GPU | 472 GFLOPS | TensorFlow, PyTorch, Caffe and MXNet | 99$ | 5 | 94.4
2 | Coral Edge TPU | Google | NXP i.MX 8M SoC: Quad-core ARM Cortex-A53 + GC7000 GPU Edge TPU coprocessor | 4 TOPS (int8) | TensorFlow Lite |  | 2 | 2000
3 | AI Core X | AAEON (ASUS) | Intel® Movidius™ Myriad™ X VPU 2485: 2 LEON4 cores 16 SHAVE core | 1 TOPS (int8) | caffe, tensorFlow | 79$ | 2.5 | 400
4 | Xilinx Zynq UltraScale+ MPSoC ZCU104 Evaluation Kit | Xilinx | Zynq UltraScale+ (XCZU7EV-2FFVC1156) | 2.4 TOPS (MAC int8) | caffe, tensorflow | 895$ | _ | _
5 | Sipeed MAIX | Seeed Studio (China) | Kendryte K210: Dua-core RV64GC, 8MB SRAM @ 400MHz, boot 800MHz KPU (Neural network processor) 64 core, APU (audio processor) | 250 GOPS Max 500 GOPS (int8) | ???? | 5$ (chip) | 0.3 | 833.3

## Slide 11: Boards survey
No. | Board | Vendor | feature |  | frameworks | Prices (eval..) | Power (W) | Power efficiently (GOP/W)
 |  |  | Chipset | OPS |  |  |  | 
1 | Jetson Nano | NVIDIA | Quad-core ARM Cortex-A57 128-core NVIDIA Maxwell™ GPU | 472 GFLOPS | TensorFlow, PyTorch, Caffe and MXNet | 99$ | 5 | 94.4
2 | Coral Edge TPU | Google | NXP i.MX 8M SoC: Quad-core ARM Cortex-A53 + GC7000 GPU Edge TPU coprocessor | 4 TOPS (int8) | TensorFlow Lite |  | 2 | 2000
3 | AI Core X | AAEON (ASUS) | Intel® Movidius™ Myriad™ X VPU 2485: 2 LEON4 cores 16 SHAVE core | 1 TOPS (int8) | caffe, tensorFlow | 79$ | 2.5 | 400
4 | Xilinx Zynq UltraScale+ MPSoC ZCU104 Evaluation Kit | Xilinx | Zynq UltraScale+ (XCZU7EV-2FFVC1156) | 2.4 TOPS (MAC int8) | caffe, tensorflow | 895$ | _ | _
5 | Sipeed MAIX | Seeed Studio (China) | Kendryte K210: Dua-core RV64GC, 8MB SRAM @ 400MHz, boot 800MHz KPU (Neural network processor) 64 core, APU (audio processor) | 250 GOPS Max 500 GOPS (int8) | ???? | 5$ (chip) | 0.3 | 833.3

## Slide 12: Boards survey (performance)
id | Neural Network | input size | MAC (GOPs) | Performance 1 (fps) | Percentage 1 | performance m (fps) | Percentage m | estimate peak MAC (GOPs)
ZCU104 |  |  |  |  |  |  |  | 
1 | ResNet-18 | 224x224 | 3.65 | 206.7 | 31.44% | 428.6 | 65.18% | 2400
2 | ResNet-50 | 224x224 | 7.7 | 82.5 | 26.47% | 151.8 | 48.70% | 2400
3 | YOLOV3_ADAS | 512x256 | 5.5 | 95.2 | 21.82% | 228.4 | 52.34% | 2400
4 | YOLOV3_ADAS | 512x288 | 53.7 | 14.3 | 32.00% | 31.7 | 70.93% | 2400
5 | YOLOV3_VOC | 416x416 | 65.4 | 15.1 | 41.15% | 33 | 89.93% | 2400
6 | YOLOV3_VOC_TF | 416x416 | 65.6 | 15 | 41.00% | 32.8 | 89.65% | 2400
7 | YOLOV2_BASELINE | 448x448 | 34 | 26.6 | 37.68% | 63.8 | 90.38% | 2400
8 | Inception-v2 | 224x224 | 4 | 158 | 26.33% | 310.2 | 51.70% | 2400
9 | Inception V4 | 299x299 | 24.5 | 30.9 | 31.54% | 64.6 | 65.95% | 2400
10 | SSD Mobilenet-V2 | 480x360 | 6.6 | 26.5 | 7.29% | 116.4 | 32.01% | 2400
11 | ResNet-50 | 224x224 | 7.7 | 82.5 | 26.47% | 151.8 | 48.70% | 2400
jetson nano |  |  |  |  |  |  |  | 
18 | Tiny YOLOV3 | 416x416 | 2.78 |  |  | 25 | 29.45% | 236
19 | Inception V4 | 299x299 |  |  |  | 11 |  | 236
20 | SSD Mobilenet-V2 | 480x360 |  |  |  | 39 |  | 236
21 | ResNet-50 | 224x224 |  |  |  | 36 |  | 236
22 | VGG-19 | 224x224 |  |  |  | 10 |  | 236
coral edge TPU (destop host: 64-bit Intel(R) Xeon(R) Gold 6154 CPU @ 3.00GHz) |  |  |  |  |  |  |  | 
28 | Inception V4 | 299x299 |  |  |  | 11.7 |  | 2000
29 | Inception v1 | 224x224 |  |  |  | 294.1 |  | 2000
30 | VGG-19 | 224x224 |  |  |  | 3.2 |  | 2000

## Slide 13: conclusion
Edge tpu offer huge computational power, but we only use small piece of it.
Movidius chip in board AI core X is the best choice with 1 TOPS, low power, low cost and good platform.
ZCU104 is the best FPGA for AI at the edge with 2.4 MAC TOPS (~4.8 TOPS) at the cost 895$